## Slide 1: BK Connect API
C:\Program Files\Bruel and Kjaer\BK Connect\Help\en-US\Consume_API\default.htm

## Slide 2
使用 BK Connect APIs
使用API允许您连接到BK connect services，来执行BK connect应用程序中的一个功能。
BK Connect runs self-hosted WCF services that are based on the Microsoft® Windows Communication Foundation framework.
The current services that support APIs are:
Data Recorder Service – All APIs
Program Service – LoadProject, LoadTemplate
Trigger Setup Service – SetTrigger
这个文档描述了如何配置你的PC，来访问API和测试API 。
Configure your PC
Testing the API from a Browser
Testing the API from Another PC or Sample App

## Slide 3
Configure your PC
Before you can access the APIs, you must first configure the PC on which the BK Connect software is installed to open the port where the WCF service is hosted, namely port 9001.
✐ Note: BK Connect must be open.
To enable the port:
Search for the Command Prompt application by entering cmd.
When the search results come up, right-click the application and select Run as Administrator.
Type in the below command:
netsh http add urlacl url=http://+:9001/ user=\Everyone
or
netsh http add urlacl url=http://localhost:9001/ user=DOMAIN\username
or
netsh http add urlacl url=http://localhost:9001/ user=\Everyone
4.When the port is successfully added, close the Command Prompt.
5.Restart BK Connect.

## Slide 4
Testing the API from a Browser
A few APIs are enabled to test from a browser or from client applications in Android™, iPhone® and Windows® smart devices.
Open up any browser and use the below URLs to test the APIs:
✐ Note: BK Connect must be started before starting a test.
Program Service
http://localhost:9001/ProgramService/LoadProject?name=ProjectName
http://localhost:9001/ProgramService/LoadTemplate?name=TemplateName
Data Recorder Service
The Data Recorder task must be opened in BK Connect before testing from a browser.
http://localhost:9001/DataRecorderService/StartRecorder
http://localhost:9001/DataRecorderService/StopRecorder
http://localhost:9001/DataRecorderService/ResetMonitor
http://localhost:9001/DataRecorderService/ManualStart
http://localhost:9001/DataRecorderService/ManualStop
http://localhost:9001/DataRecorderService/DeleteLatest
http://localhost:9001/DataRecorderService/get_RecordingDirectory
http://localhost:9001/DataRecorderService/set_RecordingDirectory?value=newPath
http://localhost:9001/DataRecorderService/get_RecordingFileName
http://localhost:9001/DataRecorderService/set_RecordingFileName?value=newPath
http://localhost:9001/DataRecorderService/get_RecordingNumber
http://localhost:9001/DataRecorderService/get_FullRecordingFileName
http://localhost:9001/DataRecorderService/get_Recording
http://localhost:9001/DataRecorderService/set_Recording?value=newPath
http://localhost:9001/DataRecorderService/get_AutoPack
http://localhost:9001/DataRecorderService/set_AutoPack?value=true/false
http://localhost:9001/DataRecorderService/get_AutoStore
http://localhost:9001/DataRecorderService/set_AutoStore?value=true/false
http://localhost:9001/DataRecorderService/set_Marker?value=newName
http://localhost:9001/DataRecorderService/get_Marker
http://localhost:9001/DataRecorderService/AddMarker
http://localhost:9001/DataRecorderService/DeleteMarker

## Slide 5
Trigger Setup Service
The Data Recorder task must be opened in BK Connect before testing from a browser.
http://localhost:9001/TriggerSetupService/SetTrigger?triggerProperties=”xml”
Sample xml for a signal trigger:
<TriggerProperties Type="eSignalTrigger" Name="Trigger 1" Level="1" Hysteresis="0.5" SelectedSignal="Signal 1" Holdoff="0.1" Delay="0" Slope="ePositive" />
Sample xml for a speed trigger:
<TriggerProperties Type="eSpeedTrigger" Name="Trigger 1" Hysteresis="0.5" Holdoff="0.1" Delay="0" SelectedTachoSignal="Tacho 1" Speed="2000" Direction="eUp"/>
Sample xml for a manual trigger:
<TriggerProperties Type="eManualTrigger" Name="Trigger 1" Delay="0"/>

## Slide 6
Testing the API from Another PC or Sample App
A few APIs are enabled to test from a browser or from client applications in Android™, iPhone® and Windows® smart device.
To test from another PC or sample Android, iOS or Windows smart device (tablet or smartphone) application, you need to consume the API differently:
Ensure both devices (host PC and testing PC/smartphone) are connected to the same network domain.
2.Switch of your firewall for private/domain network on the host PC.
✐ Note: Firewalls can be configured to trust the inbound calls on the 9001 port. Configuration of firewalls is not included in this document.
3.Replace the “localhost” with the IP address of the PC where BK Connect is running.